## Slide 1: Team Meeting
Intelligent Radio Sensing Lab. (IRS Lab)
Department of Electrical Engineering and Computer Science
DGIST
Yunjung Jeong
2026. 08. 04
Notes: Good afternoon.
Today is a short update on the Sionna simulator work.
Four parts, and one rule that governs all of them.
— 한국어 해설 —
오늘은 Sionna 시뮬레이터 작업을 짧게 가져왔습니다.
네 부분이고, 전체를 지배하는 규칙이 하나 있습니다.
표지는 기존 팀미팅 표지 그대로이고 날짜만 08. 04 로 바꿨습니다.

## Slide 2
CONTENTS
Today
Four parts, and one rule that governs all of them
Part 1 What ambient signals can measure, and who owns that law
Part 2 Where our work sits against the 26 papers we opened
Part 3 The scattering engine, and what the checks do and do not establish
Part 4 Four claims we withdrew this round
The rule: a number is on a slide only if it is quoted from a source we opened, or recomputed from a file on disk
Anything that is neither of those is labelled unverified, or it is not here.
Notes: This is a short deck by design.
Part 1 is the strongest single result we have, a velocity table across four standards.
Part 2 places us against the papers we actually opened.
Part 3 is the engine, which is the part I spent longest on and the part I put late on purpose.
Part 4 is the list of claims I withdrew.
The rule at the bottom is the reason this deck is shorter than the last one.
Q: Why is the engine last if it is the most work?
A: Because effort is not the same as interest. The velocity table changes what someone else would do next, and the engine only supports it.
— 한국어 해설 —
의도적으로 짧게 만든 덱입니다.
1부는 우리가 가진 가장 강한 단일 결과인 네 표준 무모호 속도표입니다.
2부는 우리가 실제로 연 논문들 사이에서 우리 위치를 놓습니다.
3부는 엔진인데, 가장 오래 붙든 부분이지만 일부러 뒤에 뒀습니다.
4부는 이번 라운드에 철회한 주장 목록입니다.
맨 아래 규칙이 이 덱이 지난번보다 짧아진 이유입니다.

## Slide 3
OVERVIEW
What we are building
A simulator that carries one radar cross section from an airframe mesh all the way to a calibrated detection
1 Airframe meshes
Seven drone airframes as 3-D surface meshes, built from CAD parts rather than from stacked primitives, with per-part materials.
2 Scattering kernel
Shooting and bouncing rays on Sionna's ray engine, closed by our own physical-optics surface integral over the lit facets.
3 Geometry and illuminator grid
Monostatic, bistatic and multistatic geometry crossed with three ambient illuminators, which are WiFi, LTE and 5G.
4 Calibrated detection
A constant-false-alarm-rate detector whose threshold is calibrated against a measured false-alarm rate rather than against a formula.
No new physics is claimed. The contribution is the chain, and a chain is only as honest as its weakest link.
Notes: One slide on what the whole thing is.
We take a drone airframe as a surface mesh, compute how it scatters, and carry that number through a grid of geometries and illuminators into a detector.
Radar cross section, which I will write as sigma, is the quantity that connects the two ends.
Nothing on this slide is new physics. The claim is about the chain being complete and traceable.
Q: Why not just use the ray tracer's own output?
A: That is Part 3. The short answer is that the stock solver returns path coefficients, not a scattering cross section.
— 한국어 해설 —
전체가 무엇인지 한 장으로 놓습니다.
드론 기체를 표면 메시로 받아 산란을 계산하고, 그 값을 기하와 조명원 격자를 지나 검출기까지 나릅니다.
레이다 단면적, 즉 σ 가 두 끝을 잇는 양입니다.
이 슬라이드에 새 물리는 없습니다. 주장은 사슬이 끊기지 않고 추적 가능하다는 것입니다.

## Slide 4
PART 1
What ambient signals can measure
The strongest single result we have, and the reason it is not ours
Notes: Part 1.
This is the result I would put first if I had only one slide.
It is also the one where I have to say, early, that the underlying law belongs to someone else.
— 한국어 해설 —
1부입니다.
한 장만 보여줄 수 있다면 이걸 고르겠습니다.
동시에 그 밑의 법칙이 남의 것이라고 일찍 말해야 하는 슬라이드이기도 합니다.

## Slide 5
PART 1 · VELOCITY
Unambiguous velocity of four ambient signals
CRS is the cell-specific reference signal, SSB the synchronization signal block, VHT-LTF the very high throughput long training field
Max unambiguous radial speed = wavelength x reference-signal repetition rate / 4, half-window convention, c = 3e8
Ambient signal | Repetition rate | Carrier | Unambiguous speed
LTE CRS | 1000 Hz | 1.843 GHz | 40.70 m/s
WiFi VHT-LTF | 1000 Hz | 5.21 GHz | 14.40 m/s
5G SSB | 50 Hz | 3.50 GHz | 1.07 m/s
WiFi beacon | 9.77 Hz | 5.21 GHz | 0.14 m/s
A 289-fold spread across four ambient signals, under one stated convention
Notes: Four ambient signals, one convention, one table.
The repetition rate of the reference signal sets how fast a target may move before its Doppler shift folds.
LTE cell-specific reference signals repeat at a kilohertz and reach forty metres per second.
The 5G synchronization signal block repeats at fifty hertz and stops at one metre per second.
That is a factor of two hundred and eighty-nine between the best and the worst ambient choice.
Q: Where do the repetition rates come from?
A: Honestly, only the 5G row is anchored to an outside primary source this round. The LTE and WiFi rates are assumptions inside our waveform module and I have not re-checked them against the primary specifications. That is an open item.
— 한국어 해설 —
조명원 넷, 규약 하나, 표 하나입니다.
기준신호 반복률이 도플러가 접히기 전까지 표적이 얼마나 빨리 움직여도 되는지를 정합니다.
LTE CRS 는 1 kHz 로 반복해 40 m/s 까지 가고, 5G SSB 는 50 Hz 라 1 m/s 에서 멈춥니다.
최선과 최악 사이가 289 배입니다.
⚠ 정직하게: 이번 라운드에 외부 1차 문헌으로 앵커된 것은 5G 행뿐입니다. LTE·WiFi 반복률은 우리 waveform 모듈 가정이고 열린 항목입니다.

## Slide 6
PART 1 · VELOCITY
Every airframe we model outruns ambient 5G
Every value recomputed at build time from outputs/deckfacts.json
A sampling-rate limit: the alias fraction is a constant 0.861 for 5G, 0 for WiFi and LTE.
Notes: This is the same table as a picture, with the aircraft laid on top of it.
The pink band is the published maximum speed of the five airframes we model, from 13.5 to 25 metres per second.
Ambient 5G sits at 1.07, an order of magnitude below the band.
The light blue dot is the ceiling an active sensor may request from the specification, 500 hertz, and it lands at 10.71, still under the band.
The last line matters most. This is a sampling-rate limit, so integrating longer does not fix it. We measured that: the alias fraction stays at 0.861 for 5G regardless of integration time.
Q: A folded target is still detected, is it not?
A: Correct, and we keep those two words apart. Aliasing and blindness are different quantities and we report them separately. We also do not propose a dealiasing fix. Equations 17 to 20 of the 2023 paper already do that.
— 한국어 해설 —
앞의 표를 그림으로 만들고 그 위에 실기체를 얹은 것입니다.
분홍 띠가 우리가 모형화한 5기체의 공개 최고속도 13.5~25 m/s 입니다.
상시 5G 는 1.07 로 띠보다 한 자릿수 아래이고, 규격 천장 500 Hz 로 올려도 10.71 로 여전히 띠 아래입니다.
마지막 줄이 핵심입니다. 표본화율 한계라 적분시간으로 못 없앱니다. 접힘 비율 0.861 은 CPI 와 무관한 상수입니다.
⚠ 접힘(alias)과 블라인드(blind)는 다른 양이고 따로 보고합니다. 접힘 해제 대책은 우리가 제안하지 않습니다.

## Slide 7
PART 1 · PRIORITY
The law is not ours
We reproduce a published result. We do not derive it.
The law belongs to Abratkiewicz and colleagues, IEEE JSTARS volume 16, pages 3469 to 3484, 2023, published, equation 16
Their wording matches ours down to the half-window convention, which is the place where a factor of two usually hides
We reproduce both numbers they print, 1.0901 and 4.3605 m/s at 3.44 GHz, to four decimals, once we notice they used c = 3e8
We had credited this to Chen 2024. That was wrong twice, and we corrected it this round after obtaining both papers
Chen and colleagues, Applied Sciences volume 14 article 4282, 2024, published, print no closed-form equation at all, only a numeric instantiation
Priority sits with a 2023 journal paper. Our claim has to live somewhere else.
Notes: I am putting this second rather than last, and that placement is the point.
The unambiguous-velocity law we use is equation 16 of a 2023 journal paper. Not ours.
Worse, our previous correction was also wrong. We had said Chen 2024 owned it. Chen cites the 2023 paper and prints no closed form at all, only a worked number.
We found this by finally obtaining both PDFs and reading them, which had been the largest open gap on the last deck.
Q: Two wrong attributions in a row does not sound like a careful survey.
A: The three quotations in the first round were verbatim correct. What was wrong was drawing a conclusion about a paper we had not obtained. That is exactly why the rule on slide two now exists.
— 한국어 해설 —
이 슬라이드를 마지막이 아니라 두 번째에 두는 것이 요점입니다.
우리가 쓰는 무모호 속도 법칙은 2023 년 저널 논문 eq.(16) 입니다. 우리 것이 아닙니다.
게다가 직전 정정도 틀렸습니다. Chen 2024 에 돌렸는데, Chen 은 그 2023 논문을 인용하고 닫힌 식을 아예 표시하지 않습니다.
지난 덱의 최대 공백이었던 두 PDF 를 이번에 확보해 읽고 잡았습니다.
⛔ 절대 하면 안 되는 말: '무모호 속도 식을 우리가 제시한다'.

## Slide 8
PART 1 · OUR PART
What is ours, stated narrowly
Their own conclusion names the gap: "drones whose reflectivity is significantly lower than the car used in the experiment"
1 The table
Four standards on one axis under one stated convention, spanning 289-fold. Each prior paper carries one standard only.
2 The overlay
That axis read against five published airframe maximum speeds, so the limit is judged against aircraft rather than against a formula.
3 The adjudication
Three escape hatches closed by computation. Geometry gives 0 m/s of relief, longer integration gives none, and the active ceiling covers 0 of 5.
4 The chain
The same grid carried to a detector calibrated against an empirical false-alarm rate over 2717 seconds of GPU Monte Carlo.
Neither owner of the equation used a drone. One of them wrote drones into their future work.
Notes: If the equation is theirs, what is ours.
Four things, and I want to state them narrowly enough that they survive a hostile reading.
The table, the overlay onto real aircraft, the adjudication of the three obvious escape hatches, and the chain that carries the same grid into a calibrated detector.
The quotation at the top is from the conclusion of the 2023 paper. They used a Volvo XC90. The 2024 paper used a stepper-motor rotating model. Neither used a drone, and one of them wrote drones into their future work in those words.
Q: A 2023 future-work line gives three years for someone else to have done it.
A: Which is why we counted. In the 26 rows of the matrix in Part 2, no row does drone mesh, scattering integral, amplitude validation and publication at once. That is bounded by the corpus we opened, and I will say so on that slide.
— 한국어 해설 —
식이 그들 것이라면 우리 것은 무엇인가.
네 가지이고, 적대적으로 읽어도 버티도록 좁게 진술합니다.
표, 실기체 위 겹치기, 명백한 탈출구 세 개의 판정, 그리고 같은 격자를 교정된 검출기까지 잇는 사슬입니다.
위 인용문은 2023 논문 결론입니다. 그들 표적은 Volvo XC90, Chen 은 스테퍼 모터 회전 모형이었습니다.

## Slide 9
PART 2
Where we sit
A capability matrix of 26 papers we opened, including our own empty cells
Notes: Part 2.
The format of this part came from a tracking table, and it does in one picture what ten lines of prose would do badly.
— 한국어 해설 —
2부입니다.
이 부분의 형식은 추적표에서 왔고, 산문 열 줄이 어설프게 할 일을 한 장이 합니다.

## Slide 10
PART 2 · POSITIONING
Capability matrix
18 of 26 rows shown. 0 cells unverified, 80 quotes re-checked at build
Notes: Twenty-six papers, nine capability columns.
The six columns on the left came from the tracking table, so they are not columns we invented to win. We added three: amplitude validation, geometry, and unambiguous velocity.
Every mark is graded evidence rather than an opinion. Eighty of the cells are verbatim quotations, and the build re-opens the PDFs and re-checks them on every run. All eighty passed this run, and no cell is unverified.
The bottom row is ours, boxed in green. Note that it is not the fullest row on the slide by capability count, and note the two empty cells in it.
Q: You scored yourself, so of course you look good.
A: That is why the output is an evidence table rather than a score. Disagree with a call and you can read the quotation behind it. And our row keeps two absent cells and one partial.
— 한국어 해설 —
논문 26 편, 능력 9 열입니다.
왼쪽 여섯 열은 추적표에서 왔습니다. 우리가 이기려고 만든 열이 아닙니다. 우리가 더한 것은 진폭 검증·기하·무모호 속도 세 열입니다.
모든 칸은 의견이 아니라 등급이 붙은 근거이고, 80 칸은 축자 인용이라 빌드가 매 실행 PDF 를 다시 열어 대조합니다. 이번 실행 80/80 통과, UNVERIFIED 0 입니다.
맨 아래 초록 테두리가 우리 행이고, 빈칸이 둘 있습니다.

## Slide 11
PART 2 · POSITIONING
Reading the matrix
Ours is the only row full on engine, mesh, material, aspect, geometry and unambiguous velocity at the same time
The only other row full on the first four is RadarTwin, arXiv 2026, preprint, and it is empty on geometry and on unambiguous velocity
The prior rows that are full on unambiguous velocity compute no scattering at all, so nobody currently holds both halves
Our closest competitor is Ziganshin, EuCAP 2025, published, also 6 of 9, ahead of us on diffraction, with a car as the target
We scored ourselves, so we publish the evidence and not the score. 80 of the 234 cells are verbatim quotes re-checked on every build
Our own row keeps 2 absent cells, rotor motion and diffraction, and 1 partial, amplitude validation
6 of 9 is a tie, not a lead, and the tie is with a paper that models a car.
Notes: Reading the matrix out loud.
We are the only row that is full on engine, mesh, material, aspect, geometry and unambiguous velocity simultaneously. That is the sentence I would defend.
The row that comes closest on the physics side, RadarTwin, has no geometry axis and no velocity axis. The rows that own the velocity axis compute no scattering. Nobody currently holds both halves, and that is the opening.
Our nearest tie is Ziganshin at EuCAP 2025, published. They beat us on diffraction and their target is a car.
Q: You chose the columns, so of course a combination exists where you win.
A: Six of the nine came from the tracking table, not from us. Of the three we added, we are partial on one and tied on another. And we are not nine of nine on our own column set.
— 한국어 해설 —
매트릭스를 소리 내어 읽습니다.
엔진·메시·재질·자세·기하·무모호속도 여섯을 동시에 채운 행은 우리뿐입니다. 이 문장은 방어할 수 있습니다.
물리 쪽에서 가장 가까운 RadarTwin 은 기하 축도 속도 축도 없고, 속도 축을 가진 선행들은 산란을 아예 계산하지 않습니다. 양쪽을 다 쥔 곳이 아직 없다는 것이 열린 자리입니다.
가장 가까운 동점은 Ziganshin EuCAP 2025(게재)이고, 회절에서 우리보다 앞서며 표적은 자동차입니다.

## Slide 12
PART 2 · OUR GAP
The emptiest column is diffraction
Only 3 of the 26 rows model diffraction, and our row is one of the 23 blanks
Our kernel contains zero occurrences of diffraction, physical theory of diffraction, uniform theory of diffraction, creeping or fringe. There is no edge term of any kind
Sionna does implement first-order uniform-theory-of-diffraction wedge diffraction, and its path solver ships with that switched off by default
The consequence we print: our frequency slope is 0.74 to 1.70 dB per GHz against 0.07 to 0.315 measured, which is 3.5 to 8.1 times the Das anchor
What we cannot say is that adding an edge term would fix that slope. That expectation is untested and we will not promise it
Missing diffraction is the field default and not only our lag. It is still our lag.
Notes: This is our weakest column, and it is also the emptiest column in the field.
Three rows of twenty-six model diffraction at all. Two Ziganshin papers with the uniform theory plus vertex diffraction, and one 2019 paper folding the physical theory into shooting and bouncing rays. We are in the other twenty-three.
Two things must be said precisely. Our kernel has no edge term at all, verified by a term count. And Sionna does have first-order wedge diffraction, so the sentence Sionna has no diffraction is false. It ships off by default.
The measurable consequence is our frequency slope. We are steeper than every measured anchor by a factor of three and a half to eight, though still under the pure plate limit.
Q: Then why not simply switch diffraction on?
A: Because the thing it would feed, a scattering integral, is not in Sionna. And on a tessellated shell the wedge angles are a property of our meshing rather than of the drone. The structural candidate is a physical-theory-of-diffraction term inside our own kernel, and whether that improves the slope is untested.
— 한국어 해설 —
우리의 가장 약한 열이자 분야 전체가 가장 빈 열입니다.
26 행 중 회절을 모형에 넣은 것은 3 편뿐이고 우리는 나머지 23 에 속합니다.
두 가지를 정확히 말해야 합니다. 우리 커널에는 에지항이 아예 없고(용어 카운트로 검증), Sionna 에는 1 차 UTD 쐐기 회절이 있으므로 'Sionna 에 회절이 없다'는 거짓입니다. 기본값이 꺼져 있을 뿐입니다.
측정 가능한 대가는 밴드 기울기입니다. 실측 앵커보다 3.5~8.1 배 가파릅니다.
⛔ '회절을 붙이면 기울기가 좋아진다'는 약속은 금지.

## Slide 13
PART 3
The engine
What we compute, and what the checks do and do not establish
Notes: Part 3, briefly.
This is the part I spent longest on, and it is deliberately not the headline.
— 한국어 해설 —
3부를 짧게.
가장 오래 붙든 부분이지만 일부러 헤드라인으로 두지 않았습니다.

## Slide 14
PART 3 · ENGINE
Why we wrote a scattering kernel
Radar cross section is the quantity a detector needs, and it is the quantity the stock tool does not produce
1 The gap
The installed Sionna 2.0.1 ray-tracing package contains zero occurrences of rcs and zero of radar_cross_section. No scattering integral, no sigma output.
2 What we add
Shooting and bouncing rays on that same ray engine, closed by a physical-optics surface integral over the lit facets, weighted by per-part materials.
3 What is established
Against the analytic physical-optics sphere the kernel agrees to 0.2006 dB maximum deviation, over 48 incidence directions and kr from 1 to 100.
4 What is not
Against the exact Mie solution the maximum deviation is 6.73 dB, concentrated at low kr. Both are reference solutions and never our output.
The true sentence is narrow: Sionna's default solver has no scattering integral.
Notes: Why write a kernel at all.
The honest reason fits in one grep. The installed ray-tracing package has no occurrence of rcs and no occurrence of radar cross section. It returns path coefficients, not a cross section.
So we add shooting and bouncing rays on the same engine, and close them with our own physical-optics surface integral weighted by materials.
The check that matters is card three. Against the analytic physical-optics sphere we agree to two tenths of a decibel. That establishes that our integral converges numerically to the approximation it implements.
Card four is the part I have to say out loud. Against the exact Mie solution we are off by up to six point seven decibels, concentrated at low kr, which is the few-wavelength regime.
Q: Is quoting the 0.2 dB and not the 6.7 dB choosing the flattering reference?
A: Which is why both are on the slide. The target of numerical convergence is analytic physical optics, because that is what the kernel implements. The Mie residual is the price of the approximation itself, and it falls to under two percent spread above kr thirty.
— 한국어 해설 —
왜 커널을 직접 썼는가.
정직한 이유는 grep 한 줄입니다. 설치된 rt 패키지에 rcs 도 radar cross section 도 0 회입니다. 경로 계수를 주지 σ 를 주지 않습니다.
그래서 같은 엔진 위에 SBR 을 얹고 재질 가중 PO 표면적분으로 닫습니다.
카드 3 이 핵심 검증이고, 카드 4 는 반드시 같이 말해야 하는 대가입니다.
⛔ '광선추적은 RCS 를 못 낸다'는 거짓. 참인 문장은 'Sionna 기본 solver 에 산란적분이 없다' 뿐.

## Slide 15
PART 3 · ENGINE
What is checked, and against what
Four checks, and what each one is worth
Check | Result | What it establishes
Kernel vs analytic physical optics | 0.2006 dB max | Numerical convergence of our own integral
Kernel vs exact Mie | 6.73 dB max, 1.83 % spread above kr 30 | The price of the physical-optics approximation
Measurement anchor, slope only | 0.0000 dB level shift, 7 airframes | The anchor rotates the frequency slope, never the level
Detector threshold | 3.3e-04 relative error, 2717 s Monte Carlo | False-alarm rate calibrated on data, not on a formula
Convergence is established. Absolute sigma against measurement is not.
Notes: Four checks, and what each one is worth.
Row three is the one that changed our own wording. We used to say our absolute sigma was anchored to published measurements. Then we computed what the anchor actually moves, and the mean level shift over seven airframes is zero to fourteen decimal places. The anchor rotates the frequency slope about a pivot and leaves the level exactly where our physical-optics output put it.
That is why the amplitude validation cell in our matrix row is partial rather than full, and why we hold the absolute sigma verdict open.
Q: There is a mode that anchors the level too, so why not use it?
A: Because it requires assuming a size scaling law, and our own size exponent is one point two four to one point three two with a correlation of only zero point six four to zero point seven. That is the weakest link in the anchor, so the headline uses the mode with the fewest assumptions.
— 한국어 해설 —
검증 넷과 각각의 값어치입니다.
셋째 줄이 우리 표현을 바꾼 항목입니다. 절대 σ 가 실측에 앵커되어 있다고 말해 왔는데, 앵커가 실제로 옮기는 레벨을 계산하니 7 기체 평균 이동이 소수 14 자리까지 0 이었습니다.
앵커는 기울기만 돌리고 절대 레벨은 우리 PO 출력 그대로입니다. 그래서 매트릭스의 진폭 검증 칸이 PARTIAL 이고 절대 σ 판정을 보류합니다.

## Slide 16
PART 3 · GEOMETRY
Geometry is an axis, not an escape
Monostatic and bistatic differ in link budget, and not at all in the velocity floor
Monostatic equals bistatic at zero bistatic angle. The difference is 0.000 m/s in all three bands, so our published numbers are the worst case of both
The active monostatic ceiling is a 500 Hz reference signal giving 10.71 m/s, and measured commercial networks run lower still, at 50 to 200 Hz
We quote that 500 Hz from 3GPP TS 38.331 at second hand. It is also the value least favourable to our own argument
Caveat we print: every detection result so far sits at one scene azimuth of 90 degrees, where the two path lengths are structurally equal
At that azimuth the geometry difference is 0.118 dB. Swept over azimuth it reaches 23.17 dB.
Notes: Geometry is on the slide because it is the first thing someone will offer as a way out.
It is not a way out for velocity. Monostatic equals bistatic at zero bistatic angle, exactly, in all three bands. So the numbers we publish are already the worst case of both geometries.
We also used to frame monostatic as free to choose its own repetition rate. That was wrong. The specification caps the sub-six reference signal at five hundred hertz, and the commercial networks that have been measured run between fifty and two hundred.
The last line is a limitation I want on the slide rather than in the questions. Every detection number we have comes from one scene azimuth, ninety degrees, which is the perpendicular bisector of the baseline. There the two path lengths are structurally equal and the geometries differ by a tenth of a decibel. Sweep the azimuth and that reaches twenty-three decibels.
Q: Does that invalidate the detection results?
A: It bounds them. The velocity axis is independent of azimuth. The link-budget axis is the one that is provisional, and I would rather scope it myself than have it scoped for me.
— 한국어 해설 —
기하는 청중이 가장 먼저 내밀 탈출구라 슬라이드에 올립니다.
속도에는 탈출구가 아닙니다. β=0 에서 모노와 바이가 정확히 같고 세 밴드 모두 차이 0 입니다.
'모노스태틱은 반복률을 자유롭게 고른다'는 프레이밍도 틀렸습니다. 규격이 sub-6 기준신호를 500 Hz 로 막고, 실측 상용망은 50~200 Hz 입니다.
마지막 줄은 질문받기 전에 내가 먼저 말하는 한계입니다. 지금까지 검출 결과는 전부 φ=90° 한 컷입니다. 속도 축은 φ 와 무관하고, 링크버짓 축만 잠정입니다.

## Slide 17
PART 4
What we withdrew
Four claims from earlier rounds, and what replaced them
Notes: Part 4.
Nobody in this room puts their own corrections on a slide, which is exactly why I do.
— 한국어 해설 —
4부입니다.
이 방의 누구도 자기 정정을 슬라이드에 올리지 않습니다. 그래서 올립니다.

## Slide 18
PART 4 · RETRACTIONS
Four claims we withdrew
Each row is a claim we put on a slide before, and what replaced it
What we said | What broke it | What we say now
The velocity law was ours, and then it was Chen 2024 | We obtained and read both PDFs | Priority is Abratkiewicz 2023, equation 16, and we are the reproducer
5G coverage is zero at every heading | It held at one integration time only | Alias fraction is a constant 0.861 against 0 for WiFi and 0 for LTE
Reciprocity violation of 13.7 dB | It was a one-cell approximation error | Approximation error reaches 20.04 dB, reciprocity at most 5.80 dB
The 10 log10 N combining ceiling is our convention | A published paper had it first | Textbook prior art. Our part is quantifying it across four illuminators
The third correction made our own conclusion stronger, not weaker.
Notes: Four withdrawals.
The first is the priority story from Part 1.
The second is a headline I liked too much. Zero coverage at every heading turned out to hold only at one integration time under one guard rule. We replaced the zero with a structural ratio that survives, the constant alias fraction.
The third is the one I would ask you to look at. Thirteen point seven decibels was labelled a reciprocity violation. It was not. It was a bisector-approximation error for a single cell. When we corrected the label the number went up, to twenty decibels, which strengthens the case for the monostatic arm. We corrected a number that was working in our favour to correct it.
The fourth is the ten log ten N ceiling for combining receivers. A published 2025 paper in IEEE Transactions on Aerospace and Electronic Systems states it directly, page 8814. We cannot call it ours.
Q: If the extreme numbers keep failing, why should we trust the rest?
A: The direction of each conclusion survived. What changed each time was the magnitude and the label. And an extreme number is precisely the kind a listener remembers and an opponent checks, so those are the ones worth destroying first.
— 한국어 해설 —
철회 네 건입니다.
첫째는 1부의 우선권 이야기.
둘째는 제가 너무 좋아했던 헤드라인입니다. '모든 헤딩에서 0' 은 특정 CPI·가드에서만 참인 단일-CPI 아티팩트였고, 살아남는 구조적 비율(접힘 상수 0.861)로 바꿨습니다.
셋째를 봐 주십시오. 13.7 dB 는 상반성 위반이 아니라 단일 셀의 이등분선 근사오차였습니다. 라벨을 고치자 값이 20 dB 로 올라 우리에게 오히려 유리해졌습니다. 유리해지는 방향으로도 고칩니다.
넷째, 10log10(N) 상한은 2025 년 IEEE TAES 게재 논문 p.8814 에 이미 있습니다.

## Slide 19
PART 4 · METHOD
The machinery that caught them
Four record errors this round were caught by a build script, not by a careful reader
1 Re-check every quote
The matrix build re-opens each PDF and matches the quoted sentence on every run. 80 of 80 passed, and it caught a wrong venue and a misquoted sentence.
2 Recompute every headline
The fact base recomputes each headline number from the upstream file instead of storing it. That caught two errors inside our own draft.
3 Name the corpus
Every count now carries the corpus it came from. Counting diffraction mentions gives three different answers across three different corpora.
4 Open the source
A claim is quoted from a source we opened, or computed from a file on disk. Anything else is labelled unverified or left out of the deck.
A rule that runs only when we remember it is not a rule. These run on every build.
Notes: The corrections on the previous slide are less interesting than what caught them.
Quotations are re-checked against the PDF at build time, so a wrong venue and a misquoted sentence were caught before they reached this room.
Headline numbers are recomputed from the upstream file rather than typed in, and that caught two errors inside my own draft of the fact base.
Every count now names its corpus. Counting how often diffraction appears gives three different numbers depending on whether you mean the bibliography text, the full-text corpus, or the matrix rows. Mixing those in one breath is the mistake this project has repeated most.
Q: This is process, not results.
A: Agreed, and process is the reason to believe the results. Four record errors were caught this round without anyone noticing them by eye.
— 한국어 해설 —
앞 슬라이드의 정정보다 그것을 잡은 장치가 더 중요합니다.
인용문은 빌드 때 PDF 와 재대조되어, 잘못된 게재처와 오인용이 이 방에 오기 전에 걸렸습니다.
헤드라인 수는 저장하지 않고 상류 파일에서 매번 다시 계산해, 제 초안 안의 오류 둘을 잡았습니다.
모든 개수는 코퍼스 이름을 답니다. 코퍼스를 섞는 것이 이 프로젝트가 가장 자주 반복한 실수입니다.

## Slide 20
PART 4 · OPEN
What we still cannot say
Two gaps closed this round. Here are four that did not.
1 Quote coverage
Only the 26 matrix rows are quote-verified. The wider bibliography of 81 venue entries is mostly bibliographic, and we do not call it verified.
2 Structural blind spot
The automated venue sweep used dblp, which does not index IEEE TAP, AWPL, EuCAP, IET RSN or TMTT. There, not found means not looked at.
3 One azimuth
Every detection result so far comes from a single scene azimuth of 90 degrees. The link-budget conclusions stay provisional until that is swept.
4 Second-hand spec
The 500 Hz reference-signal ceiling is quoted from 3GPP TS 38.331 at second hand. We have not opened the specification ourselves.
We can say no row of the 26 we opened fills these axes. We cannot say first in the world.
Notes: What is still open.
Card two is the one that matters most for a novelty claim. The automated venue sweep used dblp, and dblp does not index the antenna and propagation venues, which is exactly where radar cross section and diffraction papers live. In those venues, not found means not looked at, and I will keep saying it that way.
Card three is the largest recomputation item we found this round, and it is the first candidate for next work.
Q: Then can you claim novelty at all?
A: Not world-first. What the matrix supports is narrower and still useful: within the papers we opened, no row fills these axes at once. That sentence is checkable by anyone in the room, because the evidence is printed on the figure.
— 한국어 해설 —
아직 열린 것들입니다.
둘째 카드가 novelty 주장에 가장 중요합니다. 자동 지면 스윕이 dblp 를 썼는데 dblp 는 안테나·전파 지면을 색인하지 않고, 거기가 바로 RCS·회절 논문이 사는 곳입니다. '못 찾았다'는 '안 봤다'라는 뜻으로 말합니다.
셋째 카드는 이번 라운드가 찾아낸 최대 재계산 항목이고, 다음 작업 1 순위입니다.
⛔ '세계 최초'는 말하지 않습니다.

## Slide 21
CLOSING · NEXT
Two candidate directions
Both are named by a gap on this deck rather than by a new idea
A Sweep the scene azimuth
Close the single-azimuth gap. At 90 degrees the two geometries differ by 0.118 dB, and swept over azimuth the difference reaches 23.17 dB, so the link-budget ordering we report has never been tested off that one cut.
B Add an edge term as a diagnostic
Fill the empty diffraction cell with a physical-theory-of-diffraction correction inside our own surface integral. Our frequency slope is 3.5 to 8.1 times the measured anchor, and whether an edge term narrows it is untested.
C Order, and why
A first. It is cheap, it is bounded, and it can only move numbers we have already published. B is open-ended, so we would report it as a diagnostic and never as a promised fix.
D Not next: rotor motion
A real capability gap that our matrix row prints empty. We would rather leave it empty than half-claim it, so it stays in future work until someone computes it.
A first, because it is the cheapest way to test a conclusion we have already published.
Notes: Two directions, and both of them come from a blank on this deck rather than from a new idea.
Direction A is the azimuth sweep. It closes the gap I printed in Part 3, it needs no new physics, and it either confirms the link-budget ordering we have reported or it does not.
Direction B is the edge term. I am deliberately framing it as a diagnostic rather than as a fix, because we have no evidence that adding diffraction narrows our frequency slope. If we frame it as a fix and it fails, we have promised something we could not deliver.
Rotor motion stays where it is. It is a real capability gap, the matrix prints it empty, and I would rather leave it empty than half-claim it.
Q: Which one first?
A: A, because it is cheap, it is bounded, and it can only move numbers we have already published. B is open-ended.
— 한국어 해설 —
두 방향 모두 새 아이디어가 아니라 이 덱의 빈칸에서 나왔습니다.
A 는 방위각 스윕입니다. 3부에서 인쇄한 공백을 닫고, 새 물리가 필요 없으며, 우리가 보고한 링크버짓 순서를 확인하거나 뒤집습니다.
B 는 에지항입니다. '해결'이 아니라 '진단'으로 틀을 잡습니다. 회절을 붙이면 기울기가 좋아진다는 근거가 없기 때문입니다.
로터 운동은 그대로 future work 에 둡니다. 매트릭스가 그 칸을 계속 비워 인쇄할 것입니다.
순서는 A 부터입니다. 싸고 경계가 분명하고 이미 발표한 수만 움직입니다.

## Slide 22
CLOSING
We claim no new physics. We claim the chain: an airframe mesh, a material-weighted scattering integral, three geometries crossed with three illuminators, and a known velocity limit evaluated across four standards under one convention, carried to a calibrated detection.
A combination no row in the 26 papers we opened fills, and one where two of our own columns are still empty
Two qualifiers are load-bearing: illuminator type, and through a scattering integral.
Notes: One sentence to close on.
We claim no new physics. The claim is the chain, end to end, with every link traceable to a source we opened or a file on disk.
The two qualifiers on the amber bar are not decoration. Drop illuminator type and a published 2025 paper is an immediate counterexample, because they compared signal resources inside one LTE downlink on one target at a calibrated false-alarm rate. Drop through a scattering integral and several papers have already put drone and vehicle meshes into ray-traced scenes with materials.
With both qualifiers the sentence holds inside the corpus we opened, and I would rather have a narrow sentence that survives than a wide one that gets corrected in front of you.
Q: What is genuinely new, then?
A: The connection. A per-airframe material-weighted sigma travelling through a geometry and illuminator grid into a calibrated probability of detection, in one pipeline, with the empty cells printed.
— 한국어 해설 —
한 문장으로 닫습니다.
새 물리는 주장하지 않습니다. 주장은 사슬이고, 모든 고리가 우리가 연 출처 또는 디스크의 파일로 추적됩니다.
호박색 바의 한정어 둘은 장식이 아닙니다. '조명원 종류'를 빼면 2025 년 게재 논문이 즉시 반례이고, '산란적분을 통과'를 빼면 드론·차량 메시를 씬에 넣은 선행이 여럿 반례입니다.
둘 다 붙이면 우리가 연 코퍼스 안에서 문장이 성립합니다. 넓고 정정당하는 문장보다 좁고 살아남는 문장을 택합니다.